## Slide 1: Unit Process Selection

## Slide 2: Flow Equalization
Supply side
Demand side
3 contexts: where is equalization needed, what sets Q?
  Drinking water
  Waste water
  Storm water
Upstream and downstream of treatment
Upstream of treatment
Upstream of treatment
Minimum storage levels in distribution tanks
Influent Q or bypass
Influent Q or bypass
Notes: Context of CUWFP, Ithaca City water treatment plant, Bolton Point, AguaClara plants in Honduras
What flow rate must a plant be able to provide?
How is the flow rate through a drinking water treatment plant controlled?

## Slide 3: Generalize the design process
Regulations
Client needs
Possible Unit Processes
Contaminants
Sequence the unit processes
Water Source
Select Unit Processes
Disinfection Complications
Distribution Complications

## Slide 4: Unit Processes Defined
Unit process? “one or more grouped operations in a manufacturing system that can be defined and separated from others” https://en.wikipedia.org/wiki/Unit_process
  Is flocculation a unit process?
Some unit processes only make sense as part of a sequence

## Slide 5: Unit Processes (under construction)
Trash rack
Flocculation
Sedimentation
Rapid sand
Slow sand
StaRS
Activated Carbon
Ion Exchange
Reverse Osmosis
AOP
UV
Aeration
Ozone
Chlorine
Conventional treatment
Floc Blanket
Membrane
Notes: Which process in conventional treatment wastes the most water?
Where are there waste streams?
Which process removes most of the pathogens?
Rank rapid sand/membrane/and Reverse osmosis for efficiency of producing water
Which process that was presented last Thursday uses the most energy?
Which processes remove particles and pathogens
Which processes remove dissolved substances?
How might SSF remove dissolved species?
What is the particle removal mechanism for each process?
What else could be added to this diagram (plate/tube/horizontal flow sed, mechanical or hydraulic flocculation, waste streams)?
a. Screening, Coagulation, Flocculation (Chapter 9)
b. Sedimentation (Chapter 10)
c. Granular Filtration (chapter 11)
d. Membrane Filtration (Chapter 12)
e. Disinfection (Chapter 13)
3. Advanced Treatment Technologies (focus on dissolved species and chemicals)
a. Granular Activated Carbon (Chapter 15)
b. Ion Exchange Resins (Chapter 16)
c. High Pressure Membranes (Chapter 17)
d. Advanced Oxidation Process (Chapter 18)
4. Water Treatment Process Design Procedure (Chapter 23)
Adsorptive Media
Aeration and Air Stripping
Biological Filtration
Biological Treatment
Chemical Treatment
Chloramine
Chlorine
Chlorine Dioxide
Conventional Treatment
Diatomaceous Earth Filtration
Direct Filtration
GAC Isotherm (includes PAC isotherms)
Granular Activated Carbon
Hydrogen Peroxide
Ion Exchange Greensand Filtration
Membrane Filtration Microfiltration and Ultrafiltration
Membrane Separation Nanofiltration, Reverse Osmosis, Electrodialysis, and Electrodialysis Reversal
Other Treatment
Ozone
Ozone + Hydrogen Peroxide
Permanganate
Powdered Activated Carbon
Precipitative Softening
Pressure Filtration Bag Filtration and Cartridge Filtration
Slow Sand Filtration
Ultraviolet Irradiation
Ultraviolet Irradiation + Hydrogen Peroxide
Ultraviolet Irradiation + Ozone

## Slide 6: Unit Process Summary Table
Required upstream and downstream UPs
  Contaminants that must be removed prior to UP
How does it work?
What types of contaminants does it remove?
Efficiency of removing contaminant
Efficiency of producing water
What inputs (energy and chemicals) does it require?
Range of approach velocities and hydraulic residence times
Type of waste stream produced and disposal requirements
Notes: What might a cheat sheet look like? Is it a table? Or a flow chart with different entry points

## Slide 7: How do consulting firms, construction firms, venders, municipalities (clients) create a project?
We will hear about this process from Tori Klug and Michael Adelman (Engineers at Stantec) later in the semester